## Slide 1: Wavelet Based De-noising and Peak Detection of Infrared Spectra
Presentation By: Michael Ramsey
Advisor: Dr. Caroline Haddad
Secondary Advisor: dr. Barnabas Gikonyo

## Slide 2: Talk Outline:
  Infrared Spectroscopy Background
  1-Dimensional Discrete Wavelet Transform
  De-noising of Infrared Spectra
  1-Dimensional Undecimated Discrete Wavelet Transform
  Compound Identification Using Infrared Spectra

## Slide 3: Infrared Spectroscopy Background
  An Infrared Spectrometer bombards a molecule with infrared light
  Molecules absorb specific frequencies of light dependent on the molecular structure
  Too high of a frequency may cause the bonds to break
  Infrared light has a lower frequency that other parts of the electromagnetic spectrum (visible, ultraviolet)
  Instead of breaking, the bonds will vibrate, yielding information on the bonds present
  Vibrational Modes: symmetric and antisymmetric stretching, scissoring, rocking, wagging and twisting

## Slide 4: Infrared Spectrum for 2,4,6-trimethylphenol
2,4,6-trimethylphenol

## Slide 5: 1-D Discrete Wavelet Transform (DWT)
  Transforms Data so that we obtain frequency information, and the time associated with the frequencies
  Fourier transform only captures frequency information
  This transform can be described using filter banks
  Filters separates the signal into multiple components, each representing a frequency sub-band
Haar Filter Bank
  Daubechies Four-Term Orthogonal Filter Bank

## Slide 6: Computation of HWT
 |  | 0 |  | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 |  |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 |  | 
 |  | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 |  |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 |  | 
 |  | 0 |  | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 |  |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 |  | 
 |  | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 |  |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 |  | 
*
=
  Computation model using the haar wavelet transform
  This can be generalized for longer length vectors
  Note that the vector input must be of even length
  Is this transform invertible?

## Slide 7: Inverse HWT
 | 0 | 0 |  |  | 0 | 0 | 0
 | 0 | 0 | 0 |  | 0 | 0 | 0
0 |  | 0 | 0 | 0 |  | 0 | 0
0 |  | 0 | 0 | 0 |  | 0 | 0
0 | 0 |  | 0 | 0 | 0 |  | 0
0 | 0 |  | 0 | 0 | 0 |  | 0
0 | 0 | 0 |  | 0 | 0 | 0 | 
0 | 0 | 0 |  | 0 | 0 | 0 | 
 | 0 | 0 |  |  | 0 | 0 | 0
 | 0 | 0 | 0 |  | 0 | 0 | 0
0 |  | 0 | 0 | 0 |  | 0 | 0
0 |  | 0 | 0 | 0 |  | 0 | 0
0 | 0 |  | 0 | 0 | 0 |  | 0
0 | 0 |  | 0 | 0 | 0 |  | 0
0 | 0 | 0 |  | 0 | 0 | 0 | 
0 | 0 | 0 |  | 0 | 0 | 0 | 
*
=
  We have an orthogonal matrix, therefore to compute the inverse transform, simply pre-multiply by the transpose
  Matrix multiplication is inefficient for computing. Instead, we implement algorithms to compute the transform

## Slide 8: Daubechies-4 Transform of 2,4,6-trimethylphenol
Averaging
Detail

## Slide 9: Iterating the HWT
 |  | 0 |  | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 |  |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 |  | 
 |  | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 |  |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 |  | 
 |  | 0 |  | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 |  |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 |  | 
 |  | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 |  |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 |  | 
*
=
 |  | 0 |  | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
 |  | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
 |  | 0 |  | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
 |  | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 10: 3 Iterations of the Daubechies-4 Transform of 2,4,6-trimethylphenol

## Slide 11: De-noising Infrared Spectra
Our goal is to recover the original spectra

## Slide 12: How can de-noising be achieved?
Co-adding Spectra
  Obtain many different spectra of the compound
  Take the average of all the spectra obtained
  Pros
  Usually does a good job of de-noising
  Cons
  Requires a Large Sample of Spectra
  Time consuming to continually take samples
2. Mathematical Methods
  Pros
  Also does a good job of de-noising
  Much faster than co-adding spectra
  Procedure or Algorithm
  Compute the Wavelet Transform
  Apply a threshold rule to the highpass portion (detail coefficients) of the wavelet transform
  Rejoin the lowpass with the revised highpass portion
  Compute the Inverse Wavelet Transform

## Slide 13: Hard vs. Soft Thresholding

## Slide 14: Median Absolute Deviation
  Performed on each scale (j) of the detail coefficients.
  Compute
  Divide each wavelet coefficient at scale (j) by
  Find the threshold R, perform soft thresholding on each wavelet coefficient
          If
          If
          If

## Slide 15: 2,4,6-trimethylphenol De-noised by MAD

## Slide 16: Stein’s Unbiased Risk Estimate
  Performed on each scale (j) of the detail coefficients.
  Sort the squared detail coefficients in ascending order, call this
  Compute cumulative sum vector
  Linearly decreasing vector c
  Compute risk value is computed for every wavelet coefficient
          ,
  Find the threshold R, set all wavelet coefficients less than value in magnitude to 0
          if then set

## Slide 17: 2,4,6-trimethylphenol De-noised by SURE

## Slide 18: 2,4,6-trimethylphenol De-noised by Singular Value Decomposition

## Slide 19: Computation of HWT
 |  | 0 |  | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 |  |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 |  | 
 |  | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 |  |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 |  | 
 |  | 0 |  | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 |  |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 |  | 
 |  | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 |  |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 |  |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 |  | 
*
=
  Computation model using the haar wavelet transform
  This can be generalized for longer length vectors
  Note that the vector input must be of even length
  Is this transform invertible?

## Slide 20: The Undecimated Haar Wavelet Transform (UHWT)
 |  | 0 |  | 0 | 0 | 0 | 0
0 |  |  |  | 0 | 0 | 0 | 0
0 | 0 |  |  |  |  | 0 | 0
0 | 0 | 0 |  |  | 0 |  | 
 |  | 0 | 0 |  |  | 0 | 0
0 | 0 |  |  | 0 |  |  | 0
0 | 0 | 0 | 0 |  |  |  | 
 | 0 | 0 | 0 | 0 | 0 |  | 
 |  | 0 |  | 0 | 0 | 0 | 0
0 |  |  |  | 0 | 0 | 0 | 0
0 | 0 |  |  |  |  | 0 | 0
0 | 0 | 0 |  |  | 0 |  | 
 |  | 0 | 0 |  |  | 0 | 0
0 | 0 |  |  | 0 |  |  | 0
0 | 0 | 0 | 0 |  |  |  | 
 | 0 | 0 | 0 | 0 | 0 |  | 
*
=
  This computes only the lowpass portion (averaging coefficients) of the UHWT
  We add redundancy to the wavelet transform. This means there are multiple ways to compute the inverse transform

## Slide 21: Highpass Portion (Averaging Coefficients) of the UHWT
 |  | 0 |  | 0 | 0 | 0 | 0
0 |  |  |  | 0 | 0 | 0 | 0
0 | 0 |  |  |  |  | 0 | 0
0 | 0 | 0 |  |  | 0 |  | 
 |  | 0 | 0 |  |  | 0 | 0
0 | 0 |  |  | 0 |  |  | 0
0 | 0 | 0 | 0 |  |  |  | 
 | 0 | 0 | 0 | 0 | 0 |  | 
 |  | 0 |  | 0 | 0 | 0 | 0
0 |  |  |  | 0 | 0 | 0 | 0
0 | 0 |  |  |  |  | 0 | 0
0 | 0 | 0 |  |  | 0 |  | 
 |  | 0 | 0 |  |  | 0 | 0
0 | 0 |  |  | 0 |  |  | 0
0 | 0 | 0 | 0 |  |  |  | 
 | 0 | 0 | 0 | 0 | 0 |  | 
*
=
  Also notice that these matrices are no longer orthogonal
  In fact, these matrices are no longer invertible
  In this example, we obtain a transformed vector of length 16
  The UWT yields a vector that is twice the length of the original vector

## Slide 22: The UHWT of 4-ethylphenol

## Slide 23: The Undecimated Haar Wavelet Transform

## Slide 24: Peak Detection with the UHWT
159 Peaks!!!

## Slide 25: Iterating the UHWT
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
426 | 426 | 425 | 425 | 424 | 424 | 423 | 423 | 529 | 528
533 | 532 | 532 | 531 | 531 | 530 | 530 | 529 | 607 | 606
610 | 610 | 610 | 609 | 609 | 608 | 608 | 607 | 775 | 775
775 | 775 | 774 | 778 | 778 | 777 | 776 | 776 | 843 | 842
780 | 779 | 779 | 845 | 845 | 844 | 844 | 843 | 890 | 890
847 | 846 | 846 | 892 | 892 | 891 | 891 | 890 | 919 | 918
894 | 893 | 893 | 921 | 921 | 920 | 920 | 919 | 1013 | 1012
923 | 922 | 922 | 1015 | 1015 | 1014 | 1014 | 1013 | 1081 | 1080
1017 | 1016 | 1016 | 1083 | 1083 | 1082 | 1082 | 1081 | 1115 | 1115
1085 | 1084 | 1084 | 1118 | 1117 | 1117 | 1116 | 1116 | 1213 | 1212

## Slide 26: Peak Detection with the UWT – 10 iterations
143 Peaks!!!

## Slide 27: Peak Detection with the UWT – 300 iterations
50 Peaks!!!

## Slide 28: Signal Smoothing
  There are still too many peaks detected
  We need to smooth the signal further, however more iterations of the UHWT will not do a good enough job.
  We start over by utilizing a moving average filter of length N to make more drastic smoothing to the spectra
  We can also iterate this process with multiple filter lengths
  Here we apply one iteration of a moving average filter of length 424

## Slide 29: 4-ethylphenol

## Slide 30: Succinic Acid

## Slide 31: 4-nitrobenzaldehyde

## Slide 32: Results
  Peak detection performs well in identifying –OH and –CH3 functional groups
  Procedure also does well at identifying aromatic rings
  Misidentification of Alkenes and C=N bonds is present
  Need to implement a way to decipher between –OH and –COOH functional groups
        This will likely be computed by an area calculation
  Must improve peak finding in 500cm-1 - 2000cm-1 region

## Slide 33: Future Research
  Investigate other de-noising methods and threshold determination techniques
  Attempt de-noising using the undecimated wavelet transform
  Further improve my model for peak detection, and investigate other methods as well
  Obtain more information for my compound identification scheme
    Nuclear Magnetic Resonance, Mass Spectroscopy
  Incorporate probabilistic determination into compound identification

## Slide 34: References
Papers
  Alsberg, “Wavelet De-noising of Infrared Spectra”, Analyst, July 1997, Vol. 122 (645–652)
  Bos, “The wavelet transform for pre-processing IR spectra in the identification of mono- and di-substituted benzenes”, Chemometrics and intelligent laboratory systems, October 1993
  Gu, “Redundant Wavelet Transform and its Application in Denoising and Prediction”, Harvard University
  Van Fleet, Discrete Wavelet Transformations: An elementary approach with applications, 2008
Websites
  http://www.mathworks.com/help/signal/examples/signal-smoothing.html?s_eid=PSM_12299&requestedDomain=www.mathworks.com
  http://wps.prenhall.com/wps/media/objects/724/741576/chapter_13.html
  http://www.ni.com/white-paper/5432/en/

## Slide 35: Questions?
Thank you for Attending